## Slide 1: From Python to Rust, Automatically
A multi-agent pipeline for automatic Code Migration
Farzad Habibi · Internship final talk · September 2026

## Slide 2: What xcvrd is, and why it matters
An Azure datacenter switch
the box in the rack
↓
SONiC
the open-source network OS Azure runs on its switches
↓
xcvrd
the daemon that owns the optical modules
↓
Optical transceivers
the pluggable optics in the faceplate
WHAT IT DOES, ALL DAY
Notices a module being plugged in or pulled out
Reads its identity — vendor, part number, serial — from the module's on-board memory
Polls health telemetry: temperature, voltage, transmit and receive optical power
Drives the link bring-up sequence the optics spec (CMIS) defines
Publishes all of it to SONiC's state database, where the rest of the stack and all optics telemetry read it
If xcvrd is wrong, optics telemetry is wrong
— and links don't come up.

## Slide 3: The task: Code Migration
Take that daemon — about 10,000 lines of Python — and rewrite it in Rust.
xcvrd — Python
~10k lines, runs on every switch
→
?
→
xcvrd — Rust
same behavior, provably
Why bother:
  Memory safety without a garbage collector
  Predictable performance
  Reliability & maintainability
  Easy for LLMs to target and understand

## Slide 4: So just ask an LLM to translate it?
Too big for one pass
A whole daemon in one shot exceeds what any model handles reliably.
It compiles — but is wrong
Plausible Rust with drifted behavior. The compiler can't see intent.
Not verifiable
The daemon's existing tests are mostly mocks — they test plumbing, not behavior.
You can only automate what you can verify.
So: we need a hardware-free but faithful oracle before we can trust any automated port

## Slide 5: Step 1 — ground truth without hardware
An “oracle” is just something that can tell right from wrong. Ours runs the real daemon against fake optics and checks what it publishes.
xcvr-emu
fake optics in software: their
memory, sensors, link state machine
← gRPC →
the real xcvrd
the unmodified daemon, on a
fake hardware layer I wrote
→
SONiC's state database
what the daemon published
~100 tests, all the same shape: poke the fake optics → wait → check what the daemon published
Plug and unplug, module identity, optical telemetry, link bring-up, injected faults, firmware, resets and reboots.
Sanity check: a do-nothing xcvrd fails the suite — the tests actually bite. And on Python it agrees with SONiC's own community test suite.

## Slide 6: Step 2 — now automate the port
With an oracle, the port becomes a loop instead of a leap.
one big prompt
Translate 10k lines in one shot and hope.
No slice small enough to check, and nothing that says when it's done.
✗ unverifiable
vs
a deterministic loop
Translate one milestone → run the oracle → feed the failures back → repeat.
Small enough for an agent to get right — and the tests, not the model, say when it is.
✓ verified at every step

## Slide 7: The multi-agent pipeline
DETERMINISTIC WORKFLOW — a state machine, not an agent choosing what's next
Copilot CLI agent
code step
analyze
→
analyze
scope
→
scope
plan
→
plan
select_
milestone
→
select_
milestone
translate
→
translate
validate
→
validate
parity_
verify
→
parity_
verify
terminal
terminal
repair
parity gaps → new milestones
1. analyze
Read the Python daemon; design the Rust it should become.
in the Python source, its hardware interface, its tests out a target design
2. scope
Cut the daemon into ordered, testable slices — “milestones.”
every test in the oracle is assigned to the milestone that should make it pass
3. plan
Emit a Rust skeleton that already compiles, plus the plan to fill it in.
out skeleton project · Python→Rust name mapping · per-milestone plan
4. select_milestone
Pick the next slice. Nothing else is in scope.
keeps every agent call small enough to get right, and small enough to review
5. translate
An agent implements that one slice — daemon code and unit tests.
GitHub Copilot CLI · runs as a subprocess · commits only if it builds
6. validate
Two layers: Rust unit tests, then the real oracle on a live switch.
fail → straight back to translate, with the exact failures attached
7. parity_verify
Compare Python and Rust module by module — what got left behind?
passing tests ≠ complete; gaps become new milestones and the loop runs again
8. terminal
All milestones green, nothing left behind.
out a Rust daemon that passes the whole oracle
click through the pipeline

## Slide 8: Two loops make it self-correcting
The repair loop
validate → translate
A failing test isn't a dead end — the exact failures go back to the agent as its next task. It retries until the oracle is green or the budget runs out.
The parity loop
parity_verify → scope
Passing tests don't prove completeness. Parity compares Python to Rust module by module; anything untranslated becomes a brand-new milestone.
Neither loop is a human step. The pipeline exits only when both are satisfied.

## Slide 9: Result
✓ Rust daemon passes all ~100 of oracle E2E tests
✓ and SONiC's community suite, same as Python
SONIC-MGMT — THE SONiC COMMUNITY'S OWN TEST SUITE, RUN AGAINST THE RUST PORT
test_xcvr_info_in_db
module info reaches the state DB
PASS
sfp/test_sfpshow
presence, module memory
PASS (2)
sfp/test_sfputil
presence, module memory, reset
PASS (6)
api/test_sfp
the platform API surface
PASS (23)
transceiver/eeprom/
module memory read paths
PASS (3)
Same results as the Python baseline — the port is behavior-preserving, not just compiling.

## Slide 10: Benchmark
Is it faster? Not yet.
The pipeline optimized for correctness, not speed. The port is verified but untuned
NEXT
Benchmark the hot paths — parsing module memory, polling telemetry, link bring-up — against the Python daemon: CPU, memory, latency.
Then add a benchmark + optimize stage to the pipeline, and re-verify against the same oracle so speed never costs correctness.

## Slide 11: Extending the pipeline — benchmark & optimize
Same engine, two more stages: turn a verified port into a fast one — without ever giving up the verification.
DETERMINISTIC WORKFLOW
NEW STAGES
analyze
→
scope
→
plan
→
select_
milestone
→
translate
→
validate
→
parity_
verify
→
benchmark
→
optimize
→
terminal
repair
parity gaps
re-measure
benchmark
Measures the Rust port against the Python baseline on the hot paths — CPU, memory, latency — and records the numbers as an artifact.
optimize
An agent tunes what the numbers say is slow, then the loop re-enters validate: every speed-up is re-checked against the same oracle.
The exit condition never changes: no correctness regression against the oracle. Performance is only allowed to improve on top of that.

## Slide 12: What the optimize loop bought
Same switch, same oracle, before and after the benchmark → optimize loop — and every number below still passes all ~100 tests.
B9 · b09_read_amplification
Chatter with the hardware
−32%
fewer questions asked of the optical modules
Before
21.5k
After
14.6k
EEPROM events every 30 seconds
B8 · b08_error_inject
Noticing a fault
1.9× faster
from 0.26 s down to 0.14 s
Before
0.26s
After
0.14s
time to set the error flag
B5 · b05_idle_soak
Processor it uses
−15%
leaves more room for everything else
Before
41.8%
After
35.6%
CPU % over a 30 s soak
B12 · get_presence
Its most common lookup
3.6× faster
runs constantly, so this adds up
Before
8.9
After
2.4
microseconds per call
Correctness never moved: the same oracle gates every optimization round, so these are speed-ups on top of a verified port.

## Slide 13: Conclusion
A test oracle with no hardware
an emulator plus ~100 black-box tests that run the real daemon
An automated Python → Rust port
a deterministic multi-agent pipeline that validates its own work
Verified first, then faster
every optimization re-gated by the same oracle

## Slide 14: What's next
Two directions: get this daemon onto real switches, and point the same pipeline at the rest of SONiC.
1
Deploy it for real
Run the Rust xcvrd on real switches with real optics. The emulator proved behavior; hardware has to prove the rest — staged, with the same oracle running at every step.
2
Run our pipeline at the rest of SONiC
xcvrd was one daemon — nothing in the pipeline was specific to it. Each new module needs its own oracle first; that is the real cost, and it is reusable.
xcvrd
psud
ledd
thermalctld
✓ done candidates — same engine, new oracle
The daemon is the deliverable; the pipeline is the thing that keeps paying off.

## Slide 15: Thank you
Questions & discussion ?
With thanks to Changrong Wu and Guohan Lu